## Slide 1
Welcome to the future of autonomy
Caleb Chain
Project Manager

## Slide 2
Notes: Our company was found by Bobby Hambrick in 2010 when he saw a gap in large industries such as many needed automotive sensors but could not get them.
Companies like Delphi would not sell sensors unless the customer bought 100,000 units.
In the beginning it was sales and support. We have now grown to integration, engineering, and software.
We have had strong growth over the years.
We have locations around the world to support our global customers.

## Slide 3
Notes: AutonomouStuff offers many solutions.
Product – we offer products in every area of autonomy. We have knowledgeable engineers that support these products.
Services – we offer many services to help get our customers started or moving along.
Software – We offer small software applications to help kick start our customers. Shuttle, Centering, Speed, Control, etc.
Platforms – We have by wire platforms that we have a lot of experience with and also work on many other platforms as well as customer platforms. Data Intelligence – All this data has to go somewhere. We can help our customer store this.

## Slide 4
Notes: AutonomouStuff has expanded globally to provide worldwide support to our customers. We are committed to leveraging our experience to stand behind those we work with and help them however we can.
Refer to map to explain location.
Integration is in Morton, SV, Germany, and China.

## Slide 5
Notes: We support more then just automotive. We are heavy in mining with the area we are in. We have worked with aerospace, maritime, railroad, and robotics. We help many universities and startups.

## Slide 6
Notes: We are heavy in the autonomous driving industry. Some of the top companies use our support.
We have equipment and software for 3D mapping, AI, Remote Control, Object tacking, etc.

## Slide 8
Notes: AutonomouStuff has built more automated driving research and development vehicles than any other company in the world Used in 12x countries in 4x different continents
    USA, China, Canada, Israel, Korea, Australia, France, Germany, Taiwan, Japan, Italy, Qatar

## Slide 9
Notes: Talk about the sensors on the car.

## Slide 11
Notes: We strive to research & implement the latest product technologies to help you remain at the forefront of the industry.
Give examples of each product area,
3D – new stereo camera.
Actuation – Globe Motor
By Wire – PACMOD
Computing – Spectra
Data acquisition and storage – Quantum
Enclosures – APG
GPS – Novatel
Interface – Kvaser
Kits – AS kits, Apollo, etc
Lidar – Velodyne
Platforms – Lexus
Power Distribution – AS PDS
Radar – Delphi
Software – Our own
Ultrasonic – Neobotix
Vision – Flir
Wirless -

## Slide 13
Notes: We can offer services to help our customers take the next step or get started. We can help with engineering. We have many years of experience in integration of technology. We offer training on all of this. We off basic software and consulting/.

## Slide 15
Notes: Move to next slide but this will be the list.
Highway Automation – Lane Keeping, Passing, Adaptive Cruise Control
Object Processing – Lidar and Radar
Shuttle Automation – GPS waypoints
Speed and Steering – Your basics

## Slide 16
Our software solutions
Notes: Explain list.

## Slide 19
U of I Gem E2

## Slide 20: Automated Research Development Platform
Full set of software interfaces to the controls:
                Steering
                Braking
                Acceleration
Software access:
  Left and right blinkers
  Reverse and drive gear selection
  Speed feedback
Convenience features:
  Dash mounted display screen
  Game controller for by-wire testing
  Power distribution terminals

## Slide 21
OFF
ON
Switch will allow operator to cut power to Power Distribution System.
ON will supply Power to Power Distribution System from vehicle battery
OFF will remove Power to the Power Distribution System
Located under the driver’s seat.
Master power switch

## Slide 22
Power Distribution Switches
Touchscreen
(Located in front dash)
More info found here: https://autonomoustuff.atlassian.net/wiki/spaces/RW/pages/222724184/Configure+Channel+Names+on+AutonomouStuff+Power+Distribution+Touchscreen

## Slide 23
Power Distribution System
More info found here: https://autonomoustuff.atlassian.net/wiki/spaces/RW/pages/222724184/Configure+Channel+Names+on+AutonomouStuff+Power+Distribution+Touchscreen
Connect an ethernet cable to the touchscreen. You will need to configure your computer to be on the same subnet as the touchscreen. The touchscreen's default IP Address is 192.168.150.15.
Download file from touchscreen
scp root@192.168.150.15:/.config/AutonomouStuff/AutonomouStuff-Dashboard.conf .
3. Modify the file to add channel#name entries using your text editor of choice.
4. Copy the conf file back to the Touchscreen.
scp AutonomouStuff-Dashboard.conf root@192.168.150.15:/.config/AutonomouStuff/AutonomouStuff-Dashboard.conf
5. Log into device and reboot
ssh root@192.168.150.15 reboot
Programming

## Slide 24
PACMOD

## Slide 25
PACMOD Override
Brake/Throttle
E Stop
(Only removes power to PACMOD and Steering Motor)
Steering

## Slide 26
PACMOD Firmware Update
In the glovebox with the touchscreen locate the USB 2.0 B port.
The PACMod will show up as a removable drive entitled “MBED.” Replace the “.bin” with the most current one.
Reset the PACMod by power cycling it.
More Info found here: https://autonomoustuff.atlassian.net/wiki/spaces/RW/pages/17515801/PACMod+Firmware+Update+Procedure

## Slide 27
24V ESR 2.5 firmware description
Data output (similar to 12V)
  CAN bus:
    Radar tracker grouping data (merging and filtering) over CAN bus
  TCP over USB/Ethernet
    Untracked, individual detection data
  -10dBm detection threshold
  Data less noisy than 12V unit
Auto-radiating
  Does not require external input to starting radiating and outputting data
Shown to have greater stability over ethernet than the 12V unit
Multiple IP addresses available
  Upon request prior to purchase
On-board 3-axis accelerometer data available over CAN bus
Delphi ESR 2.5 firmware descriptions
Notes: The first column is similar to the 12V. The “less noisy” comment is what is typically observed. This is because Delphi has not determined what the actual dBm detection threshold really is, other than it is less than 10 dBm –due to this, the data on the 24V version actually looks like there’s less noise for the same detection/reflection sample.
The second column highlights the main points that differ between the 12 and 24V versions.

## Slide 28
Connection routed from front rack mount to trunk via conduit
Terminated with 120 ohm resistor and DB9
Connected to Lumina via Kvaser PCI-e Card
2 separate CAN channels
  PRVCAN (private)
  VEHCAN (vehicle)
Delphi 24V ESR 2.5: CAN connection wiring

## Slide 29
CAN, USB/Ethernet connection wiring
Connection routed from front rack mount to trunk via conduit
USB to ethernet adapter installed and ethernet cable connected with RJ-45 termination
Connected to Lumina via either the onboard ethernet port or via ethernet (Control) switch
Delphi 24V ESR 2.5

## Slide 30: Automated Research Development Platform
Front and Rear Rack
All front and rear racks are made with 3 by 1.5 inch 15 series 80/20

## Slide 31: Automated Research Development Platform
Roof Rack
All roof racks are made with 1.5 by 1.5 inch 15 series 80/20
15 inches
51.25 inches

## Slide 32: NovAtel
  G5Ant-3AMT4
  Matte black finish without branding
  Various mounting options and connectors
  Size: 89 mm dia. x 25 mm hgt
  Weight: 368 g
ProPak-6D1
Dual Antenna Support
Cellular
L1/L2 GPS+GLONASS
L-Band TerraStar-C PPP Corrections
-3 Grade IMUs
20 Hz Positions and Measurements
4GB Internal Memory
IMU-IGM-A1/S1:
200Hz/125 Hz Inertial Measurements
Direct Wheel Sensor Support
Commercially Exportable
Small and lightweight design

## Slide 33: Velodyne LiDAR
360° Horizontal FOV
30° Vertical FOV
Multiple Channels
100-120meters
Dual Returns
Ethernet
VLP-16

## Slide 34: Velodyne LiDAR

## Slide 35: Allied Vision

## Slide 36: Allied Vision

## Slide 37
Joystick Demo
More info found here: https://autonomoustuff.atlassian.net/wiki/spaces/RW/pages/272859181/Run+the+PACMod+Game+Control+Demo
1) On the Ubuntu Desktop, locate the icon shaped like a joystick with the name "Joystick Demo"
2) Click on the icon and the demonstration will begin allowing you to control the vehicle with the provided Game Controller.
Desktop Icon
Terminal Window
Open a new Terminal ( Ctrl+Alt+t )
Launch the game control node with the following command:
roslaunch pacmod_game_control pacmod_game_control.launch

## Slide 38
Joystick Demo
More info found here: https://autonomoustuff.atlassian.net/wiki/spaces/RW/pages/272859181/Run+the+PACMod+Game+Control+Demo
Controls

## Slide 39
More info found here: https://autonomoustuff.atlassian.net/wiki/spaces/RW/pages/272859181/Run+the+PACMod+Game+Control+Demo
1) On the Ubuntu Desktop, locate the icon shaped like a joystick with the name “AS SSC Joystick Demo"
2) Click on the icon and the demonstration will begin allowing you to control the vehicle with the provided Game Controller.
Desktop Icon
Terminal Window
Open a new Terminal ( Ctrl+Alt+t )
Launch the game control node with the following command:
roslaunch pacmod_game_control pacmod_game_control.launch
Speed and Steering Control demo

## Slide 40
Speed and Steering Control demo

## Slide 41
Speed and Steering Control demo

## Slide 42
Speed and Steering Control demo

## Slide 43
Speed and Steering Control demo

## Slide 44
Speed and Steering Control demo

## Slide 45
Speed and Steering Control demo

## Slide 46
Speed and Steering Control demo

## Slide 47
Speed and Steering Control demo

## Slide 50
Contact information
@AutonomouStuff
@AutonomouStuff
AutonomouStuff, LLC
AutonomouStuff, LLC
Caleb Chain
T: 309.291.0966
M: 309.229.1614
cchain@AutonomouStuff.com
www.AutonomouStuff.com